M7 Specification

Three 16 bit registers, A B and C
Self-compile system with no typing.

Word List

Name	Type	Description
<	word	a := b < a ? -1 : 0 (signed 16 bit)
=	word	a := b == a ? -1 : 0
-	word	a := b – a
--	xmacro	sub 1 from a
---	xmacro	sub 2 from a
,	word	compile word in a
;	macro	compile return
!	xmacro	16 bit write of b to a
!! @@	compiler	Post modify constant to load or save direct.
@	xmacro	read 16 bits a into a
*	word	a := b * a
/	word	a := b / a
+	xmacro	a := b + a
+!	word	16 bit add of b into a
++	xmacro	add 1 to a
+++	xmacro	add 2 to a
0-	word	2’s complement a
0<	word	a is true if a < 0, false otherwise
0=	word	a is true if a = 0, false otherwise
2* 4* 8* 16*	xmacro	multiply a by a power of 2
2/ 4/	xmacro	divide a by a power of 2 (arithmetic)
a,b,c,ab,abc>r	macro	push registers on stack
abs	word	calculate |a|
and	word	a := b & a
bswap	xmacro	byte swap a
c,	word	compile byte in a
c!	xmacro	8 bit write of b to a
c@	xmacro	read 8 bits a into a
compiles>	word	remove header from compilation
copy	word	transfer c bytes from a to b, handles overlaps.
fill	word	copy c bytes of a to b
h	word	access program page
halt	word	stop execution
here	word	access address of program page
mod	word	a := b mod a
not	word	1’s complement a
or	word	a := b | a
p!	xmacro	write a to port c
p@	xmacro	read port c into a
pop	macro	a→b, pop a off stack
push	macro	push a on stack
r>a,b,c,ab,abc	macro	pop registers off stack
r>r	xmacro	transfer between registers abc
swap	xmacro	exchange a and b
xor	word	a := b ^ a